## Slide 1: EURLAB
European
Robotic
LABoratory
HOW TO WIRELESS COMMUNICATE

## Slide 2
1-How TO WIRELESS communicate
1.1-PRESENTATION
This activity involves sending datas (text) from Androïd system (touchpad or mobilephone) to arduino Uno Board, then Arduino board sends received datas to Androïd system
To do this, you need :
Computer,
Arduino Uno Board,
Bluetooth Shield V2,
Androïd touchpad ou phone
USB cable,
Arduino software
Ardublock program (11-wireless communication 01.abp)

## Slide 3
2-PREPARE YOUR ANDROID SYSTEM
2.1-INSTALL BT Simple Terminal SOFTWARE
At first you have to install BT Simple Terminal on your androïd touchpad via play store.
Bluetooth Terminal App on Androïd Touchpad

## Slide 4
2-PREPARE YOUR ANDROID SYSTEM
2.2-Connect ARDUINO TO COMPUTER
Then, assemble Bluetooth Shield V2 with Arduino board and connect both to computer thanks to USB cable

## Slide 5
2-PREPARE YOUR ANDROID SYSTEM
2.3-bluetooth
From androïd touchpad,
Activate bluetooth
Search for devices (HMSoft)
Pair Bluetooth shield in androïd settings :
  To pair androïd with HMSoft, type the device’s required PIN : 1234
Launch BT Simple Terminal.
Select bluetooth device from paired device :
Check MAC Adress
  for exemple HMSoft 00:0E:EA:CF:1A:E8

## Slide 6
3-PREPARE ARDUINO
3.1-Upload Program
From computer,
Launch Arduino Software,
Launch Ardublock Sofware,
Open 11-WirelessCommunication.abp,
Upload it to arduino.

## Slide 7
4-TEST IT !
4.1-From the TOUCHPAD TO COMPUTER
Open Serial monitor from arduino,
Launch BT Simple Terminal,
Write a text, "Hello" for example.
Select Send button
Look at the result inside serial monitor

## Slide 8
4-TEST IT !
4.2-From the computer to the touchpad
Open Serial monitor from arduino,
Launch BT Simple Terminal,
Write a text, "Goodbye" for example in Arduino serial monitor.
Select Send button
Look at the result inside BT Simple Terminal