## Slide 1: EURLAB
European
Robotic
LABoratory
HOW TO Read Temperature On Graphic App

## Slide 2
1-How TO READ TEMPERATURE ON TOUCHPAD
1.1-PRESENTATION
This activity involves reading temperature values from LM35 Temperature sensor to graphic app on Androïd system (touchpad or mobilephone)
To do this, you need :
Computer,
Arduino Uno Board,
Bluetooth Shield V2,
Androïd touchpad ou phone
LM35 temperature sensor
USB cable,
Arduino software
Ardublock program (14-LM35-GraphicTemperatureApp.abp)

## Slide 3
1.2-How to connect LM35 to BLUETOOTH SHIELD V2
In order to measure Temperature on touchpad , use the picture below to connect LM35 Temperature sensor to Bluetooth Shield V2.
1-How TO READ TEMPERATURE ON TOUCHPAD

## Slide 4
1.3-Upload Program
From computer,
Launch Arduino Software,
Launch Ardublock Sofware,
Open 14-LM35-GraphicTemperatureApp.abp,
Upload it to arduino.
1-How TO READ TEMPERATURE ON TOUCHPAD

## Slide 5
1.4-How does it work?
This program converts the voltage value produced by the Temperature Sensor into a Temperature Value.
Then, Arduino program sends only the temperature value (without sentence "the temperature is") to Bluetooth serial port.
1-How TO READ TEMPERATURE ON TOUCHPAD

## Slide 6
2-TEST IT !
2.1-Read the temperature ON TOUCHPAD
Open BT Simple Terminal in Touchpad,
Look at the result !

## Slide 7
3-PREPARE YOUR ANDROID TOUCHPAD
3.1-INSTALL ES EXPLORATEUR
In order to install Eurlab_Read_Temperature app on TouchPad, you have to install ES File Explorer : File Manager from google play store.
3.2-SECURITY SETTINGS
In Security settings in Touchpad, Select « Allow installation of apps from sources other than the play store.»

## Slide 8
3-PREPARE YOUR ANDROID TOUCHPAD
3.3-copy .APK file
Copy EURLAB_Read_Temperature.apk file in Touchpad
3.4-Install APP
Open ES Explorateur file manager

## Slide 9
3-PREPARE YOUR ANDROID TOUCHPAD
3.4-Install APP
Open ES Explorateur file manager

## Slide 10
4-Test the APP
4.1-OPEn APP
Open EURLAB APP